## Slide 1
Workshop
7 of 7
Welcome!

## Slide 2: Today's Topics
Review
Data Acquisition
  MAX
  DAQ Assistant Express VI
  DAQmx API
    Create Task
    Configure Task
    Configure Trigger
    Start Task
    Read/Write
    Close Task
  Sampling Mode, Rate and Size
myDAQ Activity

## Slide 3: Review Question 3
True or False?
Automatic error handling is disabled by wiring the error input terminal.

## Slide 4: Data Acquisition (DAQ)
  Signal
  Terminal Block
  Cable
  DAQ Device
  Computer

## Slide 5: Data Acquisition (DAQ) with myDAQ
  Signal 2. myDAQ 3.Computer
USB
3.5mm cable

## Slide 6: Data Acquisition (DAQ): Software
  NI-DAQmx
    Driver level software
    Detects DAQ devices
    Installs NI-DAQmx functions in LabVIEW
  Measurement & Automation Explorer (“MAX”)
    Configure and test DAQ device
  DAQ Assistant
    Configurable Express VI used to create a DAQ application
  DAQmx API
    Provides a set of VIs to program DAQ applications
Notes: The final component of a complete Data Acquisition System is the software. In this section we will discuss the different levels of DAQmx software that are used to program your DAQ device. The three levels are NI-DAQmx, Measurement & Automation Explorer (MAX), and LabVIEW. The remainder of this chapter will contain an overview of NI-DAQ and MAX. The remaining five chapters will focus on using LabVIEW.

## Slide 7: Measurement & Automation Explorer
Configure and test DAQ device
Verify:
  - Installed devices
  - Installed software
  Available remote devices
Access wiring diagrams
Notes: Measurement & Automation Explorer (MAX) is a utility that allows you to do many things regarding data acquisition and instrument control devices. When first installing a device or software package, MAX can help you verify that everything is installed properly and communication with device is working.

## Slide 8: Measurement & Automation Explorer
Devices and Interfaces- list of installed devices (on local computer is under My System)
    Device currently installed
    Device previously installed but not currently installed
    Device ?????
My System – the local computer; the one you are currently using
Remote Systems – computers or devices (cRIO, PXI) that are available to communicate with local computer through the internet
Notes: MAX separates the local system from remotes systems. Under My System, you can expand Devices and Interfaces to see which devices are currently installed or were previously installed. Each devices will be given an alias such as Dev1 which will be used to identify the device in LabVIEW when creating tasks.

## Slide 9
Demonstration:
Using Measurement & Automation Explorer (MAX)
- Plug in your myDAQ and verify you can see it in MAX
Notes: Launch MAX
Show configuration of device
Show configuration of accessory – BNC2110
Introduction to LabVIEW Hands-On 24 ni.com

## Slide 10: DAQ terminology
Task: DAQmx’s method of organizing Analog Input, Analog Output, Digital Input, Digital Output under-the-hood; cannot have AO and AI in the same task
Channel: physical connection on the DAQ device; place where the wire(s) connect
Virtual Channel: DAQmx’s representation of a corresponding physical channel
Sampling Rate (Hz): how often data points (samples) are acquired or generated.
Sample Mode: method of acquiring data- one point at a time, in chunks or continuously

## Slide 11: DAQ Assistant
Quick way to create a VI that acquires data.
Place DAQ Assistant on block diagram -> configuration window will pop up -> configure your device -> press OK and LabVIEW will build the DAQ task

## Slide 12
Demonstration:
Configuring the DAQ Assistant
Notes: Drop a DAQ Assistant. Show how to select in or out, digital or analog.
Show how to select voltage or other parameter
Introduction to LabVIEW Hands-On 24 ni.com

## Slide 13: DAQmx API
  DAQmx API: set of DAQ functions
Notes:   Create Virtual Channel VI
    Creates a virtual channel and adds it to a task
    Use pull-down menu to select the appropriate instance of this VI
  Configure timing if reading multiple samples
    Sample rate, timing source, etc
  Configure triggering if necessary for application
    Configures the task to start or stop on a rising or falling digital edge, analog edge, or analog windows
  Acquire or generate data from the DAQ device
  Make sure pull-down menu selection is compatible with task configuration
  DAQmx Clear Task VI
    Stops the task
    Releases any resources the task reserved
    Clears the task

## Slide 14: DAQ: Basic Flow
Configure
Task
Acquire or
Generate
Data
Clear
Task
Create
Task
Start
Task
  A basic DAQmx application involves the following process: only do read/write within the loop
Notes:   Create Virtual Channel VI
    Creates a virtual channel and adds it to a task
    Use pull-down menu to select the appropriate instance of this VI
  Configure timing if reading multiple samples
    Sample rate, timing source, etc
  Configure triggering if necessary for application
    Configures the task to start or stop on a rising or falling digital edge, analog edge, or analog windows
  Starts the task after the task has been configured
  Acquire or generate data from the DAQ device
  Make sure pull-down menu selection is compatible with task configuration
  DAQmx Clear Task VI
    Stops the task
    Releases any resources the task reserved
    Clears the task

## Slide 15: DAQ: Example
Using the DAQmx API
Using DAQ Assistant

## Slide 16: myDAQ Activity: Audio Equalizer
https://decibel.ni.com/content/docs/DOC-8435

## Slide 17: myDAQ Activity: Audio Equalizer
https://decibel.ni.com/content/docs/DOC-8435
DAQ Assistant 2:
- Output >> Voltage
  - Signal Output Range: -2 to 2 V
  - Samples to Write: 100
  - Generation Mode: Continuous
Filters
Lowpass:
  Cutoff Frequency 400 Hz
Bandpass:
  Low cutoff frequency: 450
  High cutoff frequency: 2500
Bandpass:
  Low cutoff frequency: 3000
  High cutoff frequency: 10000
DAQ Assistant 1:
Input >>Voltage
  Signal Input Range: -2 to 2 V
  Acquisition Mode: Continuous
  Samples to Read : 20k
  Rate (Hz): 100k
Spectral Measurements
- Power Spectrum
Simulate Signal
Add Noise
Amplitude: 0
Noise Amplitude: 0.6
Sampling Rate: 100,000
Number of Samples: 20,000

## Slide 18
Demonstration:
Completed Audio Equalizer
Notes: Introduction to LabVIEW Hands-On 24 ni.com

## Slide 19: Homework
Study for CLAD
Go to ni.com/duke for CLAD Review Resources
  Take the practice exams
  Review the Study Guide
Notes: Introduction to LabVIEW Hands-On 24 ni.com